## Slide 1: SecURITY FOR EXISTING wireless networks
Dr. Sriram Sankaran

## Slide 2: Security for Existing Wireless Networks
Cellular
  GSM, UMTS
WiFi
  IEEE 802.11
Wireless Personal Area Networks
  Bluetooth
  Zigbee

## Slide 3: Bluetooth

## Slide 4: Bluetooth
Short-range communications, master-slave principle
Eavesdropping is difficult:
  Frequency hopping
  Communication is over a few meters only
Security issues:
  Authentication of the devices to each other
  Confidential channel
Based on secret link key

## Slide 5: Bluetooth
When two devices communicate for the first time:
  Set up the temporary initialization key

## Slide 6: Bluetooth
Setting up the link key

## Slide 7: Bluetooth Authentication protocol

## Slide 8: Bluetooth
Generation of the encryption key and key stream

## Slide 9: Weaknesses
The strength of the whole system is based on the strength of the PIN:
  PIN: 4-digit number, easy to try all 10000 possible values.
  PIN can be cracked off-line.
  many devices use the default PIN.
For memory-constrained devices: the link key = the long-term unit key of the device.
Fixed and unique device addresses: privacy problem.
Weaknesses in the E0 stream cipher.

## Slide 10: Cellular Networks

## Slide 11: GSM Security
main security requirement
  subscriber authentication (for the sake of billing)
    challenge-response protocol
    long-term secret key shared between the subscriber and the home network operator
    supports roaming without revealing long-term key to the visited networks
other security services provided by GSM
  confidentiality of communications and signaling over the wireless interface
    encryption key shared between the subscriber and the visited network is established with the help of the home network as part of the subscriber authentication protocol
  protection of the subscriber’s identity from eavesdroppers on the wireless interface
    usage of short-term temporary identifiers

## Slide 12: SIM Card (Subscriber Identity Module)
Must be tamper-resistant
Protected by a PIN code (checked locally by the SIM)
Is removable from the terminal
Contains all data specific to the end user which have to reside in the Mobile Station:
  IMSI: International Mobile Subscriber Identity (permanent user’s identity)
  PIN
  TMSI (Temporary Mobile Subscriber Identity)
  Ki : User’s secret key
  Kc : Ciphering key
  List of the last call attempts
  List of preferred operators
  Supplementary service data (abbreviated dialing, last short messages received,...)

## Slide 13: Cryptographic Algorithms for GSM

## Slide 14: GSM Authentication Protocol

## Slide 15: Ciphering in GSM

## Slide 16: Conclusion on GSM Security
Focused on the protection of the air interface
The visited network has access to all data (except the secret key of the end user)
Generally robust, but a few successful attacks have been reported:
  faked base stations
  cloning of the SIM card

## Slide 17: 3GPP Security Principles
Reuse of 2nd generation security principles (GSM):
  Removable hardware security module
    In GSM: SIM card
    In 3GPP: USIM (User Services Identity Module)
  Radio interface encryption
  Limited trust in the Visited Network
  Protection of the identity of the end user (especially on the radio interface)
Correction of the following weaknesses of the previous generation:
  Possible attacks from a faked base station
  Cipher keys and authentication data transmitted in clear between and within networks
  Encryption not used in some networks  open to fraud
  Data integrity not provided

## Slide 18: 3GPP Security Principles
New security features
  New kind of service providers (content providers, HLR only service providers,…)
  Increased control for the user over their service profile
  Enhanced resistance to active attacks
  Increased importance of non-voice services

## Slide 19: Authentication in 3GPP

## Slide 20: Generation of the Authentication Vectors

## Slide 21: User Authentication Function in the USIM

## Slide 22: More about Authentication and Key Generation
In addition to f1, f2, f3, f4 and f5, two more functions are defined: f1* and f5*, used in case the authentication procedure gets desynchronized (detected by the range of SQN).
f1, f1*, f2, f3, f4, f5 and f5* are operator-specific
However, 3GPP provides a detailed example of algorithm set, called MILENAGE
MILENAGE is based on the Rijndael block cipher
In MILENAGE, the generation of all seven functions f1…f5* is based on the Rijndael algorithm

## Slide 23: Wi-Fi Networks

## Slide 24: Introduction to Wi-Fi

## Slide 25: Introduction to Wi-Fi

## Slide 26: Wired Equivalent Privacy
part of the IEEE 802.11 specification
goal
  make the WiFi network at least as secure as a wired LAN (that has no particular protection mechanisms)
  WEP was never intended to achieve strong security
services
  access control to the network
  message confidentiality
  message integrity

## Slide 27: WEP Access Control
Before association, the STA needs to authenticate itself to the AP
Authentication is based on a simple challenge-response protocol:
  STA  AP: authenticate request
  AP  STA: authenticate challenge (r) // r is 128 bits long
  STA  AP: authenticate response (eK(r))
  AP  STA: authenticate success/failure
Once authenticated, the STA can send an association request, and the AP will respond with an association response
If authentication fails, no association is possible

## Slide 28: WEP Message Confidentiality and Integrity
WEP encryption is based on RC4 (a stream cipher developed in 1987 by Ron Rivest for RSA Data Security, Inc.)
  operation:
    for each message to be sent:
      RC4 is initialized with the shared secret (between STA and AP)
      RC4 produces a pseudo-random byte sequence (key stream)
      this pseudo-random byte sequence is XORed to the message
    reception is analogous
  it is essential that each message is encrypted with a different key stream
    the RC4 generator is initialized with the shared secret and an IV (initial value) together
      shared secret is the same for each message
      24-bit IV changes for every message
WEP integrity protection is based on an encrypted CRC value
  operation:
    ICV (integrity check value) is computed and appended to the message
    the message and the ICV are encrypted together

## Slide 29: WEP Message Confidentiality and Integrity

## Slide 30: WEP Keys
two kinds of keys are allowed by the standard
  default key (also called shared key, group key, multicast key, broadcast key, key)
  key mapping keys (also called individual key, per-station key, unique key)
In practice, often only default keys are supported
  the default key is manually installed in every STA and the AP
  each STA uses the same shared secret key  in principle, STAs can decrypt each other’s messages

## Slide 31: WEP flaws: Authentication and Access control
authentication is one-way only
  AP is not authenticated to STA
  STA is at risk to associate to a rogue AP
the same shared secret key is used for authentication and encryption
  weaknesses in any of the two protocols can be used to break the key
no session key is established during authentication
  access control is not continuous
  once a STA has authenticated and associated to the AP, an attacker send messages using the MAC address of STA
  correctly encrypted messages cannot be produced by the attacker, but replay of STA messages is still possible

## Slide 32: WEP flaws: Authentication and Access Control
Recall that authentication is based on a challenge-response protocol:
  …
  AP  STA: r
  STA  AP: IV | r Å K
  …
  where K is a 128 bit RC4 output on IV and the shared secret
Attacker can compute r Å (r Å K) = K
Then it can use K to impersonate STA later:
  …
  AP  attacker: r’
  attacker  AP: IV | r’ Å K

## Slide 33: WEP flaws: No integrity and replay protection
There’s no replay protection at all
  IV is not mandated to be incremented after each message
The attacker can manipulate messages despite the ICV mechanism and encryption
  CRC is a linear function wrt to XOR:
  CRC(X Å Y) = CRC(X) Å CRC(Y)
  attacker observes (M | CRC(M)) Å K where K is the RC4 output
  for any DM, the attacker can compute CRC(DM)
  hence, the attacker can compute:
  ((M | CRC(M)) Å K) Å (DM | CRC(DM)) =
  ((M Å DM) | (CRC(M) Å CRC(DM))) Å K =
  ((M Å DM) | CRC(M Å DM)) Å K

## Slide 34: WEP Flaws: Confidentiality
IV reuse
  IV space is too small
    IV size is only 24 bits  there are 16,777,216 possible IVs
    after around 17 million messages, IVs are reused
    a busy AP at 11 Mbps is capable for transmitting 700 packets per second  IV space is used up in around 7 hours
  in many implementations IVs are initialized with 0 on startup
    if several devices are switched on nearly at the same time, they all use the same sequence of IVs
    if they all use the same default key (which is the common case), then IV collisions are readily available to an attacker
weak RC4 keys
  for some seed values (called weak keys), the beginning of the RC4 output is not really random
  if a weak key is used, then the first few bytes of the output reveals a lot of information about the key  breaking the key is made easier
  for this reason, crypto experts suggest to always throw away the first 256 bytes of the RC4 output, but WEP doesn’t do that
  due to the use of IVs, eventually a weak key will be used, and the attacker will know that, because the IV is sent in clear
   WEP encryption can be broken by capturing a few million messages

## Slide 35: WEP: Lessons learnt
Engineering security protocols is difficult
  One can combine otherwise strong building blocks in a wrong way and obtain an insecure system at the end
  Don’t do it alone (unless you are a security expert)
    functional properties can be tested, but security is a non-functional property  it is extremely difficult to tell if a system is secure or not
  Using an expert in the design phase pays out (fixing the system after deployment will be much more expensive)
    experts will not guarantee that your system is 100% secure
    but at least they know many pitfalls
    they know the details of crypto algorithms
Avoid the use of WEP (as much as possible)

## Slide 36: Overview of IEEE 802.11i
After the collapse of WEP, IEEE started to develop a new security architecture  802.11i
Main novelties in 802.11i wrt to WEP
  access control model is based on 802.1X
  flexible authentication framework (based on EAP – Extensible Authentication Protocol)
  authentication can be based on strong protocols (e.g., TLS – Transport Layer Security)
  authentication process results in a shared session key (which prevents session hijacking)
  different functions (encryption, integrity) use different keys derived from the session key using a one-way function
  integrity protection is improved
  encryption function is improved

## Slide 37: Overview of IEEE 802.11i
802.11i defines the concept of RSN (Robust Security Network)
  integrity protection and encryption is based on AES (and not on RC4 anymore)
  nice solution, but needs new hardware  cannot be adopted immediately
802.11i also defines an optional protocol called TKIP (Temporal Key Integrity Protocol)
  integrity protection is based on Michael (we will skip the details of that)
  encryption is based on RC4, but WEP’s problems have been avoided
  ugly solution, but runs on old hardware (after software upgrade)
Industrial names
  TKIP  WPA (WiFi Protected Access)
  RSN/AES  WPA2

## Slide 38: 802.1X Authentication Model
the supplicant requests access to the services (wants to connect to the network)
the authenticator controls access to the services (controls the state of a port)
the authentication server authorizes access to the services
  the supplicant authenticates itself to the authentication server
  if the authentication is successful, the authentication server instructs the authenticator to switch the port on
  the authentication server informs the supplicant that access is allowed

## Slide 39: Mapping 802.1X model to WiFi
supplicant  mobile device (STA)
authenticator  access point (AP)
authentication server  server application running on the AP or on a dedicated machine
port  logical state implemented in software in the AP
one more thing is added to the basic 802.1X model in 802.11i:
  successful authentication results not only in switching the port on, but also in a session key between the mobile device and the authentication server
  the session key is sent to the AP in a secure way
    this assumes a shared key between the AP and the auth server
    this key is usually set up manually

## Slide 40: Protocols: EAP, EAPOL and RADIUS
EAP (Extensible Authentication Protocol) [RFC 3748]
  carrier protocol designed to transport the messages of “real” authentication protocols (e.g., TLS)
  very simple, four types of messages:
    EAP request – carries messages from the supplicant to the authentication server
    EAP response – carries messages from the authentication server to the supplicant
    EAP success – signals successful authentication
    EAP failure – signals authentication failure
  authenticator doesn’t understand what is inside the EAP messages, it recognizes only EAP success and failure
EAPOL (EAP over LAN) [802.1X]
  used to encapsulate EAP messages into LAN protocols (e.g., Ethernet)
  EAPOL is used to carry EAP messages between the STA and the AP
RADIUS (Remote Access Dial-In User Service) [RFC 2865-2869, RFC 2548]
  used to carry EAP messages between the AP and the auth server
  MS-MPPE-Recv-Key attribute is used to transport the session key from the auth server to the AP
  RADIUS is mandated by WPA and optional for RSN

## Slide 41: EAP in action

## Slide 42: Key Hierarchies

## Slide 43: Four-way handshake
Objective:
  prove that AP also knows the PMK (result of authentication)
  exchange random values to be used in the generation of PTK
Protocol:
  AP : generate ANonce
  AP  STA : ANonce | KeyReplayCtr
  STA : generate SNonce and compute PTK
  STA  AP : SNonce | KeyReplayCtr | MICKIK
  AP : compute PTK, generate GTK, and verify MIC
  AP  STA : ANonce | KeyReplayCtr+1 | {GTK}KEK | MICKIK
  STA : verify MIC and install keys
  STA  AP : KeyReplayCtr+1 | MICKIK
  AP : verify MIC and install keys

## Slide 44: TKIP
runs on old hardware (supporting RC4), but …
WEP weaknesses are corrected
  new message integrity protection mechanism called Michael
    MIC value is added at SDU level before fragmentation into PDUs
    implemented in the device driver (in software)
  use IV as replay counter
  increase IV length to 48 bits in order to prevent IV reuse
  per-packet keys to prevent attacks based on weak keys

## Slide 45: TKIP – Generating RC4 keys

## Slide 46: AES-CCMP
CCMP means CTR mode and CBC-MAC
  integrity protection is based on CBC-MAC (using AES)
  encryption is based on CTR mode (using AES)
CBC-MAC
  CBC-MAC is computed over the MAC header, CCMP header, and the MPDU (fragmented data)
  mutable fields are set to zero
  input is padded with zeros if length is not multiple of 128 (bits)
  CBC-MAC initial block:
    flag (8)
    priority (8)
    source address (48)
    packet number (48)
    data length (16)
  final 128-bit block of CBC encryption is truncated to (upper) 64 bits to get the CBC-MAC value
CTR mode encryption
  MPDU and CBC-MAC value is encrypted, MAC and CCMP headers are not
  format of the counter is similar to the CBC-MAC initial block
    “data length” is replaced by “counter”
    counter is initialized with 1 and incremented after each encrypted block

## Slide 47: Summary on Wi-Fi Security
security has always been considered important for WiFi
early solution was based on WEP
  seriously flawed
  not recommended to use
the new security standard for WiFi is 802.11i
  access control model is based on 802.1X
  flexible authentication based on EAP and upper layer authentication protocols (e.g., TLS, GSM authentication)
  improved key management
  TKIP
    uses RC4  runs on old hardware
    corrects WEP’s flaws
    mandatory in WPA, optional in RSN (WPA2)
  AES-CCMP
    uses AES in CCMP mode (CTR mode and CBC-MAC)
    needs new hardware that supports AES