## Slide 1: NETWORK LAYER SECURITY
Dr. Sriram Sankaran

## Slide 2: Network Layer Security
Threats at the Network Layer
Specific threats related to Identity
Routing and Forwarding Security
Defense Mechanisms

## Slide 3: Wireless Networking

## Slide 4: Network Layer Functionality
Network layer is primarily responsible for establishing end-to-end paths and delivering packets over them
Includes several fundamental services
  Addressing: network ID management
  Routing: finding/establishing paths
  Forwarding: delivering packets
Interacts with Transport and LINK/MAC layer

## Slide 5: Addressing
Before routing can be performed, nodes need some sort of ID or address
  Address/ID types range from local to global, just like in the postal system (streets up to ZIP codes)
  In very large-scale systems (eg. Internet), addresses must have some sort of structure
    IP addresses follow a specific hierarchy and are reused within each domain
  Within a domain and in small-scale systems (eg. MANET/WSN), addresses are typically unstructured or random
    Address management needed within a domain to prevent duplication and other failure scenarios

## Slide 6: Addressing Threats
Addresses can be changed arbitrarily
  Allows for address spoofing
    Masquerading as other node(s)
    Potential for a large number of attacks
  Changing identity to prevent detection/punishment
Attackers can infiltrate address management protocols (ARP, DHCP) to cause problems
  Inducing address duplication
  Forcing frequent address changes
  Manipulating forwarding schemes

## Slide 7: Routing
Routing = path management
  Routing does not involve actual sending of packets from source to destination(s), only sets up the path
  Lives in the “control plane”
  Involves path setup/discovery, maintenance and tear-down
Challenges in MANET/WSN environments
  Route using multiple untrusted relay nodes
  Resource and capability limitations
  No centralized authority or monitor
  Secure routing often relies on existing key mgmt.

## Slide 8: Routing Threats
Just as with other types of misbehavior, routers can be greedy, non-cooperative or malicious
  Greedy routers can refuse route discovery requests in order to save their own resources
  Non-cooperative routers can choose to selectively accept more requests to specific sources/destinations
  Malicious routers can persuade route discovery protocols so paths pass through them, avoid them or take unnecessary detours

## Slide 9: Path Attraction
Black-hole attack
  A malicious router broadcasts false claims of being “close” to the destination in order to attract all traffic and drop it
Gray-hole attack
  Similar to black-hole attack, except it only drops packets selectively
    Ex: forward all routing control packets but drop all data
Worm-hole attack
  Colluding routers create a low-latency long-distance out-of-band channel to attract routing paths and control data flow

## Slide 10: Path Manipulation
Detours
  A malicious router can modify/inject control packets to force selection of sub-optimal routes
“Gratuitous detours”
  Greedy routers can avoid being on a selected route by advertising long delays or creating “virtual nodes”
    Could be considered a form of Sybil attack, where all “personalities” are on the routing path

## Slide 11: Route Subversion
Targeted blacklisting
  In any routing protocol using blacklisting, attackers can accuse/slander/blame others to force them onto the blacklist
Rushing attacks
  Attackers can quickly disseminate forged requests, causing later valid requests to be dropped

## Slide 12: Forwarding
Forwarding = point-to-point data management
  Forwarding involves actual sending of packets from source to destination(s) on given routing paths
  Lives in the “data plane”
  Correct forwarding involves
    Sending the correct packets
    Maintaining packet order
    Respecting headers and rules
    Relaying in a timely manner
    Respecting rate control mechanisms

## Slide 13: Forwarding Threats
Misbehavior in the forwarding mechanism (often called Byzantine forwarding) includes various ways of going against forwarding rules
  Dropping packets
  Modifying packet contents or header information
  Injecting bogus packets on source’s behalf
  Forwarding to the wrong next hop
  Disrespecting rate control (flooding or throttling)

## Slide 14: Network Privacy Threats
Routing protocols inherently reveal information to curious/malicious eavesdroppers
  An attacker can listen to route discovery interactions and learn (1) locations of source and destination nodes, (2) type of interactions between nodes, (3) commonly used paths, (4) network events (5) data
  These are all issues of location privacy, network privacy and data privacy due solely to the routing process

## Slide 15: Network Layer Threats

## Slide 16: Addressing
In traditional networking, each device (radio) has two identities, in the form of addresses
  MAC address: hardware address of the radio needed for link layer communication (eg. 802.3, 802.11)
    Hard-coded into the NIC
    In theory, unique and static
  IP address: network layer address used for routing and some other higher layer services
    Virtual software address

## Slide 17: MAC Addresses
MAC addresses in the Internet
  Ethernet and WiFi use MAC addresses for link layer communication
  Independent of any higher-layer functionality
  Link layer frames carry source and destination MAC addresses (6B each)
MAC addresses in other systems
  Not typically used in sensor networks due to overhead
  Not needed if other addressing is available

## Slide 18: IP Addresses
IP addresses in the Internet
  Network layer and above use IP addresses for some identity purposes
  Independent of whatever is below the network layer
  IP addresses must be unique
IP addresses in other systems
  To support common applications, most designers are aiming to support IP addressing (to some extent)

## Slide 19: IP Address Resolution
In most Internet domains, IP addresses are assigned centrally using DHCP and bound to MAC addresses using ARP
  DHCP = Dynamic Host Configuration Protocol: host asks server for IP address, which it keeps until expiry
  ARP = Address Resolution Protocol: host asks other hosts for MAC address corresponding to an IP address

## Slide 20: ARP

## Slide 21: Limitations
MAC addresses are no longer hardware-bound
  Most Linux-like systems allow software to change MAC address used, despite hard-coded MAC address
  Many devices don’t have (unique) MAC addresses
DHCP is impractical for distributed systems
  Requires centralization
  High overhead in dynamic systems
ARP has high overhead in distributed systems
  Requires request flooding

## Slide 22: Distributed Addressing
Problem: How should IP addresses (or other suitable identities) be determined in a distributed system such that:
  Addresses are compact (-able) for low-overhead communication in sensors or embedded devices
  Network overhead is (relatively) low
  Addresses are (sufficiently) unique
  Systems can split and join
    Duplicate addresses can be detected and fixed
    Address space is large enough and dynamic

## Slide 23: Routing and Forwarding Security
Basics of routing in ad hoc networks
Control-plane attacks and defenses
Data-plane attacks and defenses

## Slide 24: Popular Routing Protocols
Link State (LS) routing
  Optimized Link State Routing (OLSR)
Distance Vector (DV) routing
  Destination Sequenced Distance Vector (DSDV)
  Ad hoc On-demand Distance Vector (AODV)
  Dynamic Source Routing (DSR)

## Slide 25: On-Demand Routing
On-demand routing has several advantages and disadvantages in MANETs
  Efficiency
    Routing information isn’t constantly collected and updated only when needed
    One-time cost of info collection can be higher
  Security
    Source nodes are aware of the entire path, unlike fully distributed algorithms that just focus on next hop
    Long-term information typically isn’t available
  Overall, advantages outweigh the disadvantages, so on-demand routing is popular

## Slide 26: Route Discovery
Source S and neighboring nodes use control message exchanges to discover a route from S to destination D

## Slide 27: Route Discovery
Route request flooding:
  Source S broadcasts a Route Request (RREQ) packet to its neighbors

## Slide 28: Route Discovery
RREQ forwarding:
  If the neighbor has no prior relationship with the destination, it will further broadcast the RREQ

## Slide 29: Route Discovery
Flooding of control packets to discover routes
  Once RREQ packet reaches the destination, or a node that knows the destination, the node will unicast a RREP packet to the source via the routed path

## Slide 30: Route Discovery
Upon receiving the RREQ, D (or another node that knows D) will unicast a Route Reply (RREP) back to S along the found path

## Slide 31: Route Maintenance
If a node can no longer reach the next hop
  Sends Route Error (RERR) control packet to inform upstream neighbors
  Route cache alternative (DSR) or rediscovery

## Slide 32: AODV vs. DSR

## Slide 33
How could an attacker interfere or manipulate MANET routing?

## Slide 34: Modification Attacks
AODV seq# modification
  AODV uses seq# as a timestamp (high seq# - fresh)
  Attacker can raise seq# to make its path attractive
DSR hop count modification
  DSR uses #hops for efficiency (low #hops – cheap)
  Attacker can lower/raise #hops to attract/repel

## Slide 35: Modification attacks
DSR route modification
  Non-existent route (DoS)
  Loops (resource exhaustion, DoS)
  No control to prevent loops after route discovery
Tunneling

## Slide 36: RREQ Flooding
Flood the network with RREQs to an unreachable destination address

## Slide 37: AODV/DSR Spoofing
Attacker listens for RREQ/RREP from neighbors
Send an “attractive” RREP with spoofed ID
Spoof more IDs with interesting results

## Slide 38: Fabrication Attacks
DoS against AODV/DSR by falsifying route errors

## Slide 39: Fabrication Attacks
DSR route cache poisoning

## Slide 40: Control Plane Security
How to guarantee that an established path can be efficient?
How to prevent attackers from manipulating path discovery/construction?
What metrics can be used to quantify the value of a path?
  Length? Latency? Trust?

## Slide 41: Securing DV routing
Distance vector routing is one of the classical approaches to network routing
SEAD: Secure Efficient Ad hoc DV Routing
  [Hu et al. Ad hoc Networks 2003]
  Based on DSDV protocol using sequence numbers to prevent routing loops
  Uses hash chains to authenticate routing updates
  Relies on existing mechanisms to distribute authentic hash chain end-elements

## Slide 42: Securing LS Routing
Link State routing is another classical approach to network routing
SLSP: Secure Link-State Protocol
  [Papadimitratos and Haas, WSAAN 2003]
  MAC Address/ IP address pairs are bound using digital signatures
  Allows for detection of address re-use and change
  Uses hash chains for authentication

## Slide 43: Secure Routing Protocol
SRP authenticates single-hop exchanges in DSR request and reply messages
  Since protection is hop-by-hop, SRP over DSR is vulnerable to path modification

## Slide 44: SAODV
Secure AODV introduces signatures into the AODV protocol to authenticate various message fields
  RREQ and RREP are signed, hop counts are authenticated using hash chains

## Slide 45: ARAN [Sanzgiri et al., ICNP 2002]
ARAN: Authenticated routing for Ad hoc networks
  Make use of cryptographic certificates and asymmetric key to achieve authentication, message integrity and non-repudiation
  Need preliminary certification process before a route instantiation process
  Routing messages are authenticated at each hop from source to destination and vice versa

## Slide 46: Authenticated Route Discovery

## Slide 47: Authenticated Route Setup

## Slide 48: Route Maintenance
Send ERR message to deactivate route

## Slide 49: ARAN Security
Modification attacks
  Prevents redirection using seq# or #hops
  Prevents DoS with modified source routes
  Prevents tunneling attacks
Impersonation attacks
  Prevents loop-forming by spoofing
Fabrication attacks
  Prevents route error falsification

## Slide 50: ARAN Limitations
ARAN relies on an underlying PKI
  Requires a trusted third-party / infrastructure
  Requires either:
    Significant communication overhead to interact with the TTP for near-term updates/revocation
    Long delays in certificate updates, revocation lists etc.

## Slide 51: Ariadne [Hu, Perrig and Johnson, 2004]
Ariadne is a secure on-demand routing protocol built on DSR and Tesla
  DSR: Dynamic Source Routing, Tesla: Timed Efficient Stream Loss-Tolerant Authentication (broadcast auth)
  Route request and reply messages are authenticated

## Slide 52: Forwarding security in the data plane

## Slide 53: Data plane security
Injecting and modifying packets are issues of packet/data integrity, can be solved using cryptographic techniques
Forwarding to the wrong next hop is an issue of protocol compliance but can be checked and reported similar to packet/data integrity
Packet dropping is an issue of compliance and availability

## Slide 54: Data Plane Availability
Cryptographic primitives alone cannot solve availability problems at the data plane
  Cannot provide any sort of guarantee about delivering data through routers that misbehave
  In general, crypto alone cannot solve DoS problems
  Data plane availability is partially due to compliant behavior of routing nodes and partly due to natural non-deterministic faults, errors and failures

## Slide 55: E2E Delivery Measures
Suppose packet delivery is measured end-to-end using signatures or MACs
  Every message carries overhead for packet authentication, but message authentication is already desirable for many other reasons
  Packet drop induces end-to-end retransmission
    With high delay if the ACK is also dropped/modified
  Packet modification forces routers to carry bogus message all the way to the destination node

## Slide 56: Limitations
Paths can only be changed after a large number of end-to-end transactions, i.e. after enough data is available to make a decision
Path-based detection only identifies a bad path, not a bad node
  Good nodes may be excluded from networking
  May have to search a large number of paths to find one with good performance

## Slide 57: Per-Node Delivery Measures
Suppose packet delivery is measured per node
  Verification at finer granularity may require more overhead (eg. MAC per node)
  Quicker retransmission requests can be issued by intermediate routers, but malicious routers can also request retransmissions
  Routers are forced to do more computation and reporting
  Neighbors may be required to “overhear” behavior

## Slide 58: ShortMAC [Zhang et al., NDSS 2012]
Instead of reacting to poor performance, highly efficient monitoring can enable continuous monitoring with minimal overhead
A few key design insights allow for significant efficiency gains by making seemingly-significant trade-offs with detectability

## Slide 59: ShortMAC Counters
Fault localization -> Packet authentication
  Fault localization -> monitor packet count, content
  W/ pkt authentication, content -> count
  Counters-only approach yields small state and low communication overhead

## Slide 60: Limiting the Attacker
Limiting attacks instead of perfect detection
  Detect every misbehavior? Costly! Error-prone!
  Absorb low-impact attack: tolerance threshold
  Trap the attacker into a dilemma
  Enable probabilistic algorithms

## Slide 61: Detection using Counters
High-level steps
  Each node maintains two counters
  Secure reporting
  Threshold based detection robust to natural errors
  Details in the paper

## Slide 62: Limitations
ShortMAC was designed for the Internet and has some implicit assumptions that limit its use in wireless domains
  Detection is based on a threshold value much higher than a natural packet loss threshold – in wireless, natural packet loss can be high
  Source must share pairwise symmetric key with every node along the path

## Slide 63: Random Audits in MANETs [Kozma and Lazos, WiSec 2009]
Instead of constantly monitoring every node’s forwarding behavior, only perform path audits when end-to-end performance degrades
To audit a path, source constructs a disjoint audit path to a node on the path and uses this path to carry audit request/response

## Slide 64: Efficient Auditing
Upon request, a node generates a proof of which packets it has seen
  Reporting a list of all packets is inefficient, so compression is required
  Bloom Filter does lossy packet list compression

## Slide 65: Random Audits
REAct = Resource Efficient ACcounTability
  Audits are triggered by performance degradation
  Source S audits a node N on the path
  If the returned Bloom filter from N is sufficiently close to that of S, then audit a node downstream
  Else, audit a node upstream of N
  Eventually, search will converge to the lossy link
  Source can change route around the lossy link to identify which node is misbehaving

## Slide 66: Limitations
REAct assumes that attackers have a static attack strategy
  Dropping packets only when not being audited will work
REAct assumes that multiple attackers do not collude
  Colluding attackers can trade duties when being audited