## Slide 1: MAC-Layer SECURITY
Dr. Sriram Sankaran

## Slide 2: MAC-LAYER SECURITY
IEEE 802.11 MAC LAYER
Misbehavior in 802.11 MAC
Threats at the MAC Layer

## Slide 3: IEEE 802.11
Infrastructure mode
  Many stations share an AP connected to internet
    Distributed Coordination Function (DCF)
    Point Control Function (PCF)
      Rarely used due to inefficiency, vague standard specification and lack of interoperability support
Ad hoc mode
  Multi-hop, no infrastructure, no Internet
  Never really picked up commercially
Mesh mode (using 802.11s)

## Slide 4: 802.11 MAC
Responsibilities of the MAC layer
  Logical responsibilities
    Addressing
    Fragmentation
    Error detection, correction and management
  Timing responsibilities
    Channel Management
    Link flow control
    Collision avoidance
Our focus will be on timing-based vulnerabilities

## Slide 5: CSMA
Carrier Sense Multiple Access
  Listen to the channel before transmitting
  If channel is quiet, transmit
    After a short delay, (DIFS = DCF Inter-frame spacing)
  If channel is busy
    Wait until its quiet for a DIFS period
    Wait for random backoff period
    Send if still quiet
  Wait for ACK or retransmit using random back-off

## Slide 6: DCF operation using CSMA

## Slide 7: Random back-off
Reduce the chance of collisions
  Each device must wait a random duration depending on past contention – use “contention window” CW
  If the medium is busy
    Wait for DIFS period
    Set backoff counter randomly in CW
    Transmit after counter time expires
  After failed retransmissions:
    Increase CW exponentially
    2n-1 from CWmin to CWmax, eg., 7-> 15 -> 31

## Slide 8: Collision Avoidance
Attempt to make channel reservation to avoid collisions by other senders
Request to Send (RTS)
  Before transmitting data, sender transmits RTS
Clear to Send (CTS)
  Receiver transmits CTS to tell sender to proceed
RTS and CTS use short IFS (SIFS < DIFS) to give priority over data packets

## Slide 9: RTS/CTS Usage
RTS/CTS is not required
  S1-R1 use RTS/CTS, S2-R2 do not

## Slide 10: MAC-layer misbehavior
802.11 DCF works well under the assumption that everyone plays nicely together
  This may have been a reasonable assumption when MAC protocols were hardware-bound
However, selfish and malicious nodes are free to arbitrarily break the rules
  Software MAC makes this very easy to do

## Slide 11: Question
What are some of the different ways to misbehave at the MAC layer?

## Slide 12: MAC Jamming
DCF structure and behavior gives advantages to jamming attackers
  Jamming after RTS (and SIFS period) blocks CTS (prevents data flow) and occupies channel (prevents other senders from using it)
    Low duty-cycle attack -> order-of-magnitude efficiency gain

## Slide 13: MAC Blocking
DCF structure and behavior gives advantages to other DoS attackers
  RTS/CTS “flooding” – repeated sending of RTS/CTS exchanges while other senders obey the rules

## Slide 14: MAC Greed with Jamming
Greedy/malicious sources can block or collide with other sources, causing their sending rates to decrease
  Gives more opportunity to greedy source

## Slide 15: MAC Greed with Parameters
Greedy/malicious sources can manipulate protocol parameters for unfair resource usage

## Slide 16: Cheating in CSMA/CA
“CSMA/CA was designed with the assumption that the nodes would play by the rules”
  MAC cheaters deliberately fail to follow the IEEE 802.11 protocol, in particular in terms of the contention window size and back-off

## Slide 17: System Game Model
N tx-rx pairs in a single collision domain, using 802.11, C of N are cheaters with control of MAC layer parameters
Cheaters want to maximize avg. throughput ri
As a game:
  Each player (cheater) adjusts its contention window size Wi
  Players react to changes of remaining N-C users who play by the rules
Authors analyze relationships between throughput and contention window sizes

## Slide 18: Single static checker
First case: a single cheater with a fixed strategy (ie. makes a decision and sticks with it)
A single cheater gets best throughput at Wi = 1
In fact Wi = 1 is the Nash Equilibrium for the static game

## Slide 19: Multiple Static Cheaters
Second case: many cheaters with fixed strategy
  Cheaters don’t know about each other
  Cheaters are aware of the cheater v. cheater competition in forming strategies
Window size Wi = 1is no longer optimal

## Slide 20: Dynamic Cheating game
In the dynamic game, cheaters can change their strategy in response to other players (including other cheaters)
  A penalty is enforced on the utility function, so cheaters converge to the optimal operating point
  “Cooperative cheaters” can inflict penalty on “non-cooperative cheaters” by jamming their packets

## Slide 21: Distributed/Adaptive Cheating
Cheaters can observe actual throughput and jamming to adapt contention window size
  Cheaters are forced to cooperate or get lower throughput due to penalization from other cheaters

## Slide 22: Detecting Greedy Behavior [Raya et al., 2006]
Detection of greedy behavior in the Mac layer of Ieee 802.11 public Networks (DOMINO)
  Software installed at/near the access point that can detect and identify greedy players
  No changes to software of benign players

## Slide 23: DOMINO Architecture

## Slide 24: Behavior Tests
The DOMINO-enabled AP performs a number of behavioral tests as a decision-making basis
Scrambled/re-transmitted frames
Shorter than DIFS
Oversized NAV
Observed back-off
Consecutive back-off

## Slide 25: UDP vs. TCP Traffic
Impact of misbehavior varies for different types of target traffic
  Disparity between cheater and benign users is higher in UDP case

## Slide 26: UDP vs. TCP Detection
Traffic type also has significant impact on detection capabilities of DOMINO
  Actual back-off test in UDP vs. Consecutive back-off test in TCP
    TCP Congestion control causes additional timing-related behaviors that can cause detection errors

## Slide 27: Further Discussions in Paper
The DOMINO paper talks about a lot of different types of misbehavior
  Jamming attacks, timing misbehavior etc.
Design of a deployable system
  Lots of design parameters to choose
  Analysis of numerous types of misbehavior
  Incorporation of security mechanisms, quality of service, wireless error scenarios (eg. Hidden terminal)

## Slide 28: Fairness in 802.11
802.11 incorporates various fairness mechanisms
  Provides fairness regardless of connection quality
  Allows low-quality connections to occupy the medium for much longer than high quality connections

## Slide 29: Implicit Jamming in 802.11
802.11 has a built-in fairness mechanism that basically allows all users to get the same long-term throughput
  A clever attacker can take advantage of this property to deny service to others by jamming a single user
  Degradation of the single user effectively starves the other users
  Jamming an end node is not necessarily observable by the AP, so detection is much harder

## Slide 30: Implicit Jamming
Low-power jammer attacks a single nearby node, degrades throughput for every user using the same AP

## Slide 31: Mitigating Implicit Jamming
FIJI: anti-jamming mitigation of the implicit jamming attack
  Goal 1: ensure that nodes not under attack are not indirectly affected by the attack
  Goal 2: ensure that the maximum amount of traffic is delivered to the node under attack, given that the node is under attack
  Both goals rely on explicit detection of the jamming attack

## Slide 32: FIJI Detection Component
Detection module
  Since FIJI is run/managed entirely at the AP, detection must also take place there; not typical jamming attack detection
  Standard jamming detection mechanisms (eg. Using RSSI + PDR) don’t apply, need other metrics
  Instead, look for changes in transmission delay
    Very large increment in measured transaction time indicates the node is under attack

## Slide 33: FIJI Traffic Component
Adjust the traffic patterns to all clients based on detection events
  Trivial solution: don’t send any data to jammed clients, but this is unfair and could lead to big problems if any detection errors occur
  Accept traffic degradation to attacked node, but keep traffic patterns constant for other nodes
  Two approaches to deal with the attacked node:
    Adjust the data packet size: shorter packet fragments are more likely to get through
    Adjust the data rate: send to the jammed nodes less often

## Slide 34: FIJI Evaluation