## Slide 1: Physical Layer Security

## Slide 2: Wireless PHY
The wireless PHY is responsible for delivering a bit stream from a transmitter to one or more receivers. It's not as easy as it sounds.
Tx/Rxs need to be coordinated in time, space, frequency, phase, encoding/language
Wireless means there are many sources of error, reasons for failure, etc.

## Slide 3: PHY Standards
In Wi-Fi networks, IEEE 802.11 defines several versions of the PHY, including extensions for mesh, vehicular, etc.
In telecom, the GSM 05.xx series defines the Um physical layer, and other standards build on it, including ITU-T standards like 4G.
• In PANs, standards like 802.15.1 (Bluetooth), .3 (high-rate, e.g., UWB), and .4 (low-rate, e.g., Zigbee) all define their own PHY models.

## Slide 4: Wireless Phy Services
Various parts of PHY operation
  Radio interface: spectrum allocation, signal strength, bandwidth, carrier sensing, phase sync
  Signal processing: equalization, filtering, training, pulse shaping, signaling,…
  Coding: channel coding, bit interleaving, forward error correction, …
  Modulation (mapping bits to signals)
  Topology, antennas, duplex/simplex, multiplexing and so much more
PHY is typically the most complex part of a wireless network

## Slide 5: Physical Layer Threats

## Slide 6: The Party Analogy

## Slide 7: Physical Layer Misbehavior
Open, shared medium is vulnerable
  Anyone can “talk” -> greedy or malicious nodes can easily interfere
    Prevention/degradation of communication via jamming
    Cutting off available resources influences network control, operation and performance
  Anyone can “listen” -> curious or malicious nodes can easily eavesdrop on communication
    Recovery of information exchanged by neighbors (violation of data, identity, operation/intention privacy)
    Inference/learning, tracking, observing

## Slide 8: Challenges
How can we prevent a curious or malicious party from eavesdropping on wireless transmissions at the physical layer?
How can we prevent a greedy or malicious party from interfering with PHY transmission and reception?

## Slide 9: Spread Spectrum
Spread Spectrum is an extension of multiplexing that uses randomization to increase diversity and improve performance in various ways
  Frequency-hopping spread spectrum (FHSS) builds on FDM allowing devices to pseudo-randomly move among frequency channels
  Direct-sequence spread spectrum (DSSS) builds on CDM allowing devices to pseudo-randomly move among different code spaces
    Code Spaces are analogous to frequency bands

## Slide 10: Multiplexing

## Slide 11: FHSS
Sender and receiver synchronize a hopping pattern over a large bandwidth

## Slide 12: DSSS
DSSS encoding maps long symbols to sequences of short chips
Shorter chip duration means wider bandwidth

## Slide 13: Benefits
FHSS
  Narrow-band interference only has an effect for a small fraction of the time
  Single-channel eavesdroppers can’t follow the signal, need to use much wider bandwidth to hear everything
DSSS
  Narrow-band interference is despread at the receiver
  Other signals are (nearly) orthogonal
  Eavesdropper has to know/guess code to decide

## Slide 14: Cryptographic SS
Building off basic spread spectrum, we can add cryptographic randomization to make hopping schedule and code sequences secret
  Using a symmetric key as a seed to PRNG makes the hopping schedule or code sequence secret
In both cases, this requires symmetric key management, which has its own issues

## Slide 15: Issues with Spread Spectrum
To be effective against curiosity/greed/malice , hopping sequences (FHSS) and spreading codes (DSSS) must be private
  In many implementations, these codes are given to all group members – if becoming a group member is easy, there’s no barrier
  If group membership is tightly guarded, can it be bought or stolen?
If codes can’t be obtained, can they be learned?
  Code reuse allows for statistical analysis and recovery

## Slide 16: Further hardening the PHY
If spread spectrum isn’t enough, what else?
  Multiple diversity can protect against multiple threats at numerous levels
  Implementations must consider the threat models and adapt to unexpected behaviors
    Prevent statistical analysis, adapt to learning adversaries

## Slide 17: Jamming and Physical Layer Security

## Slide 18: Outline
Jamming attacks and defenses
Secrecy using physical layer properties
Authentication using physical layer properties

## Slide 19: Jamming
A physical layer denial-of-service attack that aims to prevent communication between parties

## Slide 20: How does Jamming work?

## Slide 21: Geometry matters

## Slide 22: Timing Matters

## Slide 23: Generalized Jamming
A jammer allocates energy/signal to diverse time and freq resources according to an attack strategy S
  Effect E(S) of the attack
  Cost C(S) of the attack
  Risk R(S) of being detected/punished
  With other metrics, an optimization emerges

## Slide 24: Jamming Strategies: Time Domain

## Slide 25: Jamming Strategies: Frequency Domain

## Slide 26: How can we protect against Jamming?

## Slide 27: Jamming Detection and Defense [Xu et al. IEEE Network 2006]
Goal: Detect and localize jamming attacks, then evade them or otherwise respond to them
Challenge: distinguish between adversarial and natural behaviors (poor connectivity, battery depletion, congestion, node failure etc.)
  Certain level of detection error is going to occur
  Appropriate for deployment in sensor networks
Approach: coarse detection

## Slide 28: Basic Detection Strategies
Received Signal Strength (RSSI)
  Jamming signal will affect RSSI measurements
  Very difficult to distinguish between jamming/natural
Carrier Sensing Time
  Helps to detect jamming as MAC misbehavior
  Doesn’t help for random or reactive cases
Packet Delivery Ratio (PDR)
  Jamming significantly reduces PDR (to ~0)
  Robust to congestion, but other dynamics (node failure, outside comm range) also cause PDR -> 0

## Slide 29: Advanced Detection
Combining multiple statistics in detection can help
  High PDR + High RSSI -> OK
  Low PDR + Low RSSI -> Poor Connectivity
  Low PDR + High RSSI -> ? -> Jamming attack?

## Slide 30: Jammed Area Mapping
Based on advanced detection technique, nodes can figure out when they are jammed
At the boundary of the jammed area, nodes can get messages out to free nodes
Free nodes can collaborate to perform boundary detection using location information

## Slide 31: Evading Jamming
Nodes in the jammed region can evade the attack, either spectrally or spatially
  Spectral evasion -> “channel surfing” to find open spectrum and talk with free nodes
  Spatial evasion -> mobile retreat out of jammed area
    Need to compensate for mobile jammers ability to partition the network

## Slide 32: Dynamic attack and defense strategies

## Slide 33: Optimal Jamming and Detection
Problem Setup: each of the network and the jammer have control over random jamming and transmission probabilities
  Network parameter ‘alpha’ is probability each node will transmit in a time slot
  Attack parameter ‘q’ is probability the jammer will transmit in a time slot
Opponents can learn about goals through observation and optimize for min-max/max-min

## Slide 34: Jamming Games
What if both attacker and defender are freely adapting in response to each other?

## Slide 35: Secure communication using properties of the wireless medium

## Slide 36: Wiretapping
In 1975, A. D. Wyner defined the wiretap channel to formalize eavedropping

## Slide 37: Secrecy Capacity
Since the Alice -> Eve channel is noisier than Alice->Bob channel
  Eve can’t decode everything that Bob can decode
  There’s a really nice Information Theory formalization of the concept of secrecy capacity, namely the amount of secret information Alice can send Bob without Eve being able to decode

## Slide 38: Degraded Eavesdropper?
In a practical scenario, is it reasonable to assume the eavesdropper’s signal is more degraded than the receiver’s?
  Probably not
Can we exploit the diversity of receivers?

## Slide 39: Diversity of Receivers
The signal emitted by a transmitter looks “different” to receivers in distinct locations

## Slide 40: Measurement + Feedback
Channel State Information (CSI)
  CSI is the term used to describe measurements of the channel condition
  If Alice knows the CSI to Bob and to Eve, she can find an appropriate encoding using the measurements
  If Alice and Bob interact repeatedly, measurement and feedback actually increase the secrecy capacity
    This can allow for secrecy capacity > 0 even if Eve’s channel is less noisy than Bob’s channel

## Slide 41: Jamming for Good
If Alice has diversity in the form of multiple radios or some collaborators
  Alice and friends can use a jamming attack to prevent Eve from eavesdropping
  As long as they don’t jam Bob at the same time
  Ex: if the deployment geometry is known, Alice can adjust power, antenna config etc. so Bob’s SINR is high but Eve’s is low

## Slide 42: Antenna Control
Antenna control can be used for transmission with low probability of interception

## Slide 43: Application
Building on secrecy capacity:
  If two devices can communicate with a high probability guarantee that eavesdroppers cannot hear them, whatever they say is secret
  Secret messages -> keys!
  Secret key generation is now possible using inherent properties of the wireless medium

## Slide 44: Further Reading
For a really good summary of secrecy capacity, the formalization, secret key generation and lots of excellent details
  “Physical layer Security” by Bloch and Barros

## Slide 45: Authentication using Physical Layer properties

## Slide 46: Diversity of Senders
Signals captured by a receiver from senders in distinct locations look “different”

## Slide 47: Signalprints [Wise 2006]
In a WLAN with multiple APs, each AP sees different characteristics of packets from each sender
  Each AP can measure various packet features, some of which are relatively static over packets: eg. RSSI
  A back-end server can collect measurements and keep history of packets from different senders

## Slide 48: Verification and Matching
Requirements for verification:
  Robust to transmission power control, random fluctuations and error

## Slide 49: Signalprint Properties
Difficult to spoof?
  Spoofing node would require control of medium
  Transmission power control creates lower RSS at every AP; differential analysis reveals power control
Correlated with physical location
  Attacker needs to be physically near target device
Sequential packets have similar signalprints
  RSSI values are highly correlated for stationary sender and receiver
    Note: not highly correlated with distance, but very highly correlated with subsequent transmissions

## Slide 50: Limitations
Signalprints with any reasonable matching rule cannot differentiate between nearby devices
  Masquerading/spoofing attacks are possible if physical proximity is easily achieved
Low-rate attacks cannot be detected
  But, low-rate attacks have limited effects
Multi-antenna attackers can cheat

## Slide 51: Summary
Interference and eavesdropping are two of the most fundamental yet least understood problems in wireless. There’s still a lot of work to be done.