## Slide 1: Privacy in WIRELESS NETWORKS
Dr. Sriram Sankaran

## Slide 2: Lecture Overview
Privacy risks at the wireless network layer
Several different approaches in different systems/scenarios

## Slide 3: Privacy Issues
Network layer interactions in wireless networks often expose information about identity, context, content, relationships etc.
In certain cases, cryptographic protections can help, but not always
In certain cases, pseudonyms help, but not always

## Slide 4: ID Matching
Network IDs/addresses can facilitate tracking, profiling, inference etc.
  Ex: a network service provider sees device A connect to a network in Pgh, then to another network in DC, then to another network in SF -> the service provider can create a profile of the device owner
  Ex: an eavesdropper sees device A show up and connects to a network at the same time every day -> the eavesdropper can temporarily profile the user to learn when they will be away from home

## Slide 5: Traffic Analysis
A curious or malicious party can observe network traffic and analyze flow patterns to infer relationships
  Plaintext IDs can make this pretty easy
  Something like “conservation of flow” can allow traffic flow decoupling
  Inference capability depends on several factors:
    Network visibility – global or local view?
    Traffic density – dense or traffic distributions?

## Slide 6: Timing Analysis
Since network operations are typically at least somewhat delay sensitive, there are end-to-end correlations between transmission events
  Ex: node A transmit 10 packets, then neighboring node B transmits 10 packets of similar size -> maybe B is relaying A’s traffic
  Depending on visibility and density, very little other information is needed, (eg. Strong hop-by-hop packet re-encryption doesn’t prevent timing analysis)

## Slide 7: Understanding the risks
What type of network? Services? Etc. ?
  WLAN, cellular, VANET, WSN ..
What is the attacker’s goal/ purpose?
  Real-time tracking, recovering past traces
  Robbery, personal safety, blackmail, mal-marketing, surveillance
What granularity is needed for attack success?
  Relational, location-specific, region-specific

## Slide 8: Privacy Challenges
Understanding the privacy goals
  What needs to be protected?
  What are the rules to be enforced?
Understanding the threat
  What are attacker’s goals, capabilities, methods etc?
  Practicality of attacker assumptions?
Metrics
  How to measure privacy protection and enforcement?
  How to evaluate and incorporate risk?

## Slide 9: Different Privacy Concerns
Profiling and tracking WiFi users
Event/object inference in WSN
Unauthorized user/car tracking in VANET

## Slide 10: Traffic Anonymization
In multi-hop networks (MANET/WSN), transmission linking can expose what path is used for a session
  Traffic analysis
    Analyzing flow of packets through a network (with global knowledge) allows decomposition into individual flows
  Local traffic analysis
    Without global knowledge, timing information can expose flow decomposition in a neighborhood

## Slide 11: WSN Location Privacy
In sensor networks, we’re usually not concerned with protecting sensor locations, but what they’re sensing may be more sensitive

## Slide 12: Source Location Privacy
One of the common goals in WSN is to hide the location of the sensed event from an observer
  But, traffic generated will immediately expose any singular event
  Commonly called the “Panda Hunter Problem”
    Sensors in a wildlife area are used to track/study pandas
    Whenever a panda walks by a sensor, it generates traffic
    A hunter can track the traffic to find the panda

## Slide 13: Privacy in Wireless Networks
Privacy in RFID Systems
Location Privacy in Vehicular Networks
Privacy Preserving Routing in Ad hoc Networks

## Slide 14: Privacy in RFID Systems
RFID = Radio-Frequency Identification
RFID system elements
  RFID tag + RFID reader + back-end database
RFID tag = microchip + RF antenna
  microchip stores data (few hundred bits)
  tags can be active
    have their own battery  expensive
  or passive
    powered up by the reader’s signal
    reflect the RF signal of the reader modulated with stored data

## Slide 15: RFID Applications today
proximity cards
  electronic tickets for public transport systems (AFC)
  access control to buildings
automated toll-payment transponders
anti-theft systems for cars
  RFID transponder in ignition keys
payment tokens
  contactless credit cards (e.g., Mastercard PayPassTM)
identification of animals
identification of books in libraries

## Slide 16: RFID Applications in the near future
replacement of barcodes
  advantages
    no need for line-of-sight
    hundreds of tags can be read in a second
    unique identification of objects
    easy management of objects throughout the entire supply chain (manufacturer  retailer  consumer)
  standardization is on the way
    EPC (Electronic Product Code) tag
  main issue is price
    today an EPC tag costs 13 cents
    massive deployment is expected when price goes below 5 cents
e-passports
embedding RFID tags in Euro banknotes
  anti-counterfeiting
  detection of money laundering

## Slide 17: RFID Applications in the future
shopping
  fast check-out at point-of-sale terminals
    terminal reads all tags in the shopping cart in a few seconds
    payment can be speeded up using contactless credit cards
  return items without receipt
    no need to keep receipts of purchased items
  tracking faulty or contaminated products
    object IDs can serve as indices into purchase records
    one can easily list all records that contain IDs belonging to a particular set of products and identify consumers that bought those products
smart household appliances
  washing machine can select the appropriate program by reading the tags attached to the clothes
  refrigerator can print shopping lists automatically or even order food on-line
interactive objects
  consumers can interact with tagged objects through their mobile phones (acting as an RFID reader)
  the mobile phone can download and display information about scanned objects (e.g., movie poster, furniture, etc.)

## Slide 18: RFID
RFID tags respond to reader’s query automatically, without authenticating the reader
 Clandestine scanning of tags is a plausible threat
Two particular problems:
  Inventorying
  Tracking
watch: Casio
book: Applied Cryptography
shoes: Nike
suitcase: Samsonite
jeans: Lee Cooper

## Slide 19: Classification of Privacy Protection approaches
standard tags
  “kill” command
  “sleep” command
  renaming
  blocking
  legislation
crypto enabled tags
  tree-approach
  synchronization approach
  hash chain based approach

## Slide 20: Dead tags
idea: permanently disable tags with a special “kill” command
part of the EPC specification
advantages:
  simple
  effective
disadvantages:
  eliminates all post-purchase benefits of RFID for the consumer and for society
    no return of items without receipt
    no smart house-hold appliances
    …
  cannot be applied in some applications
    library
    e-passports
    banknotes

## Slide 21: “Sleep” tags
idea:
  instead of killing the tag put it in sleep mode
  tag can be re-activated if needed
advantages:
  simple
  effective
disadvantages:
  difficult to manage in practice
    tag re-activation must be password protected
    how the consumers will manage hundreds of passwords for their tags?
    passwords can be printed on tags, but then they need to be scanned optically or typed in by the consumer

## Slide 22: Renaming tags
idea:
  get rid of fixed names (identifiers)
  use random pseudonyms and change them frequently
requirements:
  only authorized readers should be able to determine the real identifier behind a pseudonym
  standard tags cannot perform computations  next pseudonym to be used must be set by an authorized reader

## Slide 23: Issues with Renaming
a possible implementation
  pseudonym = {R|ID}K
    R is a random number
    K is a key shared by all authorized readers
  authorized readers can decrypt pseudonyms and determine real ID
  authorized readers can generate new pseudonyms
  for unauthorized readers, pseudonyms look like random bit strings
potential problems
  tracking is still possible between two renaming operations
  if someone can eavesdrop during the renaming operation, then she may be able to link the new pseudonym to the old one
  no reader authentication  rogue reader can overwrite pseudonyms in tags (tags will be erroneously identified by authorized readers)

## Slide 24: Renaming
a public key based implementation:
  El Gamal scheme:
    public key is (p, g, A), the cleartext is m
      p large prime
      g is a generator of the multiplicative group Z*p
      A=ga (mod p), where a is a secret value known only to Alice
    select a random integer r, and compute R = gr mod p
    compute C = m×Ar mod p
    the ciphertext is the pair (R, C)
  one can re-encrypt a ciphertext (R, C) without decryption:
    select a random integer r’, and compute R’ = Rgr’ mod p ( = gr+r’ mod p)
    compute C’ = CAr’ mod p ( = mAr+r’ mod p)
    (R’, C’) is a valid ciphertext of m
  new tag pseudonyms can be computed by readers that know the public key
  real tag ID can be computed only by readers that know the private key

## Slide 25: Crypto-enabled tags
assume that tags can perform some crypto operations
 tags can compute their own pseudonyms !
a solution that doesn’t scale:
  next pseudonym = {R, S, ID}K
    R is a random number generated by the tag (ensures that pseudonyms look random and they are different)
    S is some redundancy (ensures that the reader can determine if it used the right key to decrypt the pseudonym)
    ID is the real identifier
    K is a key shared by the tag and the reader
  the reader tries all possible keys until it finds the right one
  if there are many tags, then the verification may be too slow

## Slide 26: Vehicular Networks

## Slide 27: Vehicular Communication

## Slide 28: Vehicular Communication

## Slide 29: Security and Privacy

## Slide 30: Security and Privacy

## Slide 31: Location Privacy in Vehicular Networks
Vehicles continuously broadcast heart beat messages, containing their ID, position, speed, etc.
Tracking the physical location of vehicles is easy just by eavesdropping on the wireless channel
One possible solution is to change the vehicle identifier, or in other words, to use pseudonyms

## Slide 32: Adversary Model
Changing pseudonyms is ineffective against a global eavesdropper
Adversary is assumed to be able to monitor the communications only at a limited number of places and in a limited range

## Slide 33: Concept of Mix-Zone
Unobserved zone functions as a mix zone where the vehicles change pseudonym and mix with each other
Note that the vehicles do not know where the mix zone is (this depends on where the adversary installs observation spots)
We assume that the vehicles change pseudonyms frequently so that each vehicle changes pseudonym while in the mix zone

## Slide 34: Example of mix-zone

## Slide 35: Model of the Mix-Zone
time is divided into discrete steps
pij = Pr{ exiting at j | entering at i }
Dij is a random variable (delay) that represents the time that elapses between entering at i and exiting at j
dij(t) = Pr{ Dij = t }
Pr{ exiting at j at t | entering at i at t } = pij dij(t-t)

## Slide 36: Observations
the adversary can observe the points (ni, xi) and the times (ti, ti) of enter and exit events (Ni, Xi)
by assumption, the nodes change pseudonyms inside the mix zone  there’s no easy way to determine which exit event corresponds to which enter event
each possible mapping between exit and enter events is represented by a permutation p of {1, 2, …, k}:

## Slide 37: Another Privacy Metric
tracking game:
  the adversary picks a vehicle v in the observed zone
  she tracks v until it enters the mix zone at port s
  then, she observes the exiting events until time T (where the probability that v leaves the mix zone until T is close to one)
  for each exiting vehicle at port j and time t, the adversary computes qjt = psjdsj(t)
  the adversary decides to the exiting vehicle v’ for which qjt is maximal
    this realizes a Bayesian decision (minimizes the error probability of the decision)
  the adversary wins if v’ = v
the level of privacy achieved is characterized by the success probability of the adversary
  if success probability is high, then level of privacy is low

## Slide 38: Privacy Preserving Routing in Ad hoc Networks
Goal: unlinkability (make it very hard for a global observer to know who communicates with whom)
Some nodes may be compromised  even the forwarding nodes should not know who the source and the destination are
We also want to hide the identity of the forwarding nodes from each other (because this information would be useful for the attacker)

## Slide 39: Effective but inefficient solution
Route establishment: flooding the network with a route request
Source:
  generates an asymmetric key-pair (K,K-1), a secret key k0, and a nonce n0
  Encrypts D, S, and K-1 with the public key KD of the destination
  Encrypts k0 and n0 with K
  Broadcasts the route request:

## Slide 40: Effective but inefficient solution
F1 receives this route request
It verifies if it is the target of the request:
  decrypts with its K-1
If F1 is not the target:
  Generates a secret key k1 and a nonce n1
  Concatenates them to
  Encrypts the result with K
  Broadcasts

## Slide 41: Effective but inefficient solution
D attempts to decrypt and it succeeds
D broadcasts a dummy request:
It decrypts and obtains the secret keys and the nonces of the forwarding nodes
It generates a link key for each link and sends a route reply:

## Slide 42: Effective but inefficient solution
Fi receives route reply: decrypts it with ki
If ki works: checks if it received back its ni
If this is the case:
  Fi peels the outer layer off the route reply
  Applies some padding to retain its original length
  Re-broadcasts
Sending data:
  Source encrypts the packet with kout0 and broadcasts it
  Each node tries to decrypt it with its incoming link keys
  If Fi succeeds to decrypt the packet with kiin: it re-encrypts it with kiout, and re-broadcasts it
  Until the packet arrives to the destination

## Slide 43: Improving Efficiency
Much computation from the nodes:
  Solution: replace the public key encryption with symmetric key encryption
Source and destination share a secret key kSD and a counter cSD
Source computes a one-time hint for the destination: h(kSD,cSD)
Each node can pre-compute the hint of each possible source:
  only a table lookup when processing route request messages